## Slide 1: Domenico Argenziano Tutor: Alessandro Cilardo XXX Cycle - III year presentation
Cryptographic Extensions for a
GPU-like processor

## Slide 2: Background
Ingegneria Informatica MSc.
Computer Architectures group
No fellowship

## Slide 3: Summary of activities
Concluded in Nov. 2016 collaboration with Prof. Galdi about Trusted Computing
Worked on a project proposal for Secure-by-design execution
Designed an AVR-based Gateway for secure communication of field bus sensor data
GPU crypto extensions (this presentation)
Experience abroad

## Slide 4: Experience abroad
Period Jun-Sept. 2017 spent at Sundance Multiprocessor Technology, Chesham, UK
Tulipp H2020 project
Low-power SoC-based computing for Computer Vision
Attended EMVA 2017 forum in Vienna

## Slide 5: Credits table

## Slide 6: The MANGO project and consortium
Universitat Politècnica de València (SPAIN)
CeRICT / University of Naples (ITALY)
Politecnico di Milano (ITALY)
Zagreb University (CROATIA)
Pro Design GmbH (GERMANY)
Thales Communication & Security (FRANCE)
EPFL (SWITZERLAND)
Philips Medical Systems (NETHERLAND)
Eaton Industries SAS (FRANCE)
MANGO: exploring Manycore Architectures for Next-GeneratiOn HPC systems
One of the 19 large projects selected for exploring innovative HPC solutions (H2020-FETHPC 2014 call)

## Slide 7: MANGO project overview
GN
HN
HN
HN
GN
GN
HN
HN
GN
GN
GN
GN
GN
HN
HN
HN
GN
HN
GN
GN
GN
GN
GN
HN
deeply Heterogeneous acceleration Node (HN)
General-purpose compute Node (GN)
Innovative Cooling and Power Monitoring
Optical network
NoN-IB bridge

## Slide 8: The MANGO GPU-like accelerator
Nu+ (or ν+) GPU-like core
Open source, software-programmable HDL design
Fits both MANGO perspectives:
  FPGA-based emulation
  FPGA-based computation: provides a parametrized, programmable overlay

## Slide 9: GPU processing
GPUs were born for graphics application
Identical computation on several independent data workloads (pixels, vertices, fragments)
GPUs have progressively found application in other fields (such as linear algebra) where similar workloads are present
Most vectorizable problems can benefit from GPU power

## Slide 10: Graphics workloads
Several identical, independent computations on different data

## Slide 11: A simple pipeline

## Slide 12: CPU-like core
Lots of resources dedicated to control logic rather than computing logic
Stalls compensated exploiting ILP

## Slide 13: More computing power: multi-core
Good for general purpose parallel computing, but duplicates control logic
Simplify each core, at cost of less ILP (more stalls)

## Slide 14: More computing power: multi-core
Same function on different data => SPMD approach
Good for general purpose parallel computing, but duplicates control logic
Simplify each core, at cost of less ILP (more stalls)

## Slide 15: SIMD processing approach
Amortizes control/managing cost of instruction threads using multiple ALUs
Requires vector instructions
Scalar threads are grouped into vector threads
Scalar threads execute in lock-step fashion

## Slide 16: What about branches?
if (cond > 0) {
a = 3;
b = 5;
c = 1;
} else {
a = 2;
b = 2;
}
Lane-level predicated execution =>
Execution masks

## Slide 17: What about stalls?
Fill long latencies interleaving execution of different, independent threads (SIMD threads)
Multiple contexts (e.g. register files)
No fancy control logic
SIMT (Single Instruction Multiple Threads) approach

## Slide 18: Multiple SIMT cores

## Slide 19: Nu+ microarchitecture
Configurable parameters:
Number of cores
Number of Threads
Number of hw lanes
Number of registers per Thread
Cache set-size
Number of ways
Number of 32-bit words in each line
SPM banks number
Instruction Fetch
Decode
FIFO
FIFO
Dynamic Scheduling
Scoreboard
RR Scheduler
SRF
VRF
FIFO
SPM
INT
FP
SFU
FIFO
FIFO
FIFO
FIFO
RR Scheduler
Writeback
Operand
Fetch
Thread Scheduler
Thread Controller
Memory
External Thread Enable
Load miss / store
Load miss
FIFO full
BC
PC
PC
Blocked threads
Restore Scoreboard
Flush FIFOs
Branch Taken
Restore Thread PC
LDST
FIFO
Rollback Handler

## Slide 20: Nu+ crypto extensions
Problem: adding cryptographic extensions while adhering to GPU paradigm
Vectorizable operations (data dependencies)
HW resources dedicated mostly to computing
No complex control logic implemented in HW
Most control logic exposed to SW level

## Slide 21: Extensions for asymmetric cryptography
Modular multiplication is the fundamental operation of most public-key cryptosystems
Used in two main kinds of cryptosystems:
  Exponentiation-based: RSA, El Gamal, Diffie-Hellman
  Elliptic Curve schemes based on prime Finite Fields GF(p)

## Slide 22: Modular multiplication
Montgomery reduction is a widespread and efficient approach to perform modular reduction without any trial division.
It can be efficiently integrated with multiplication
Complexity of Montgomery multiplication just slightly above that of simple multiplication

## Slide 23: Montgomery multiplication
How is reduction integrated (separated, coarsely or finely integrated)
How multiplication is performed (school-book algorithm, Karatsuba, Toom-Cook, etc…)
Do we scan operands or result?

## Slide 24: FIOS Montgomery multiplication
Most computing concentrated inside inner loop

## Slide 25: FIOS Montgomery multiplication
Inner loop iteration
Main issue: tight data dependencies hinder vectorization

## Slide 26: Parallelized inner loop
We broke data dependencies
High data bandwidth requirement => added internal registers

## Slide 27: Extended Nu+ core
Units subject to major modification are marked in red
Anyway, most pipeline units have been modified to support new instructions
Three operands (2 vector + 1 scalar) are read during Operand Fetch stage
Functional units not involved in our algorithm are not shown

## Slide 28: Extended ISA

## Slide 29: Validation
Algorithm for Montgomery multiplication has been written at assembly level
For now, two versions: 256 and 512 bits
Test vectors generated using GMP library
Core simulation performed using Xilinx XSim

## Slide 30: Results: area usage
Nu+ core synthetized in Xilinx Vivado for Zynq-7030 SoC
Max core frequency of 200 MHz
4 lanes, 4 threads, 32 bit word, 64 vector and scalar registers
ICache size= 32Kb SPM size= 8Kb
Baseline version: ALU, simple MAC, SPM, Load/Store

## Slide 31: Results: performance
 | Cycles/Mult. (256 bits) | Cycles/Mult. (512 bits)
Baseline Nu+ | 558 | -
Extended Nu+ | 212 | 466
[Seo,Liu et al.](A9) | 658 | 2254
[Seo,Liu et al.](A15) | 308 | 1485
[Massolino et al.] | 328 | 1093

## Slide 32: Extensions for symmetric cryptography
We focused on the AES standard, the most widespread cipher for symmetric cryptography
Chosen by NIST to supersed old DES standard
One block size: 128 bits
Three possible key sizes: 128, 192 and 256 bits
Worked on AES128 (10 rounds)

## Slide 33: AES state matrix
Input block size is 128 bits, divided into 16 bytes
16 bytes are arranged in a 4x4 matrix as below
We store this matrix row-wise

## Slide 34: AES encryption algorithm

## Slide 35: AES support for Nu+
We produced two version of Nu+ for AES
The main difference is how lookup tables are implemented
  (Ver1) Lookup table in ScratchPad memory, separated address space, deterministic access time (useful for twart Timing Side-Channel attacks)
  (Ver2) Lookup table in dedicated unit: better performance but more resorces required

## Slide 36: Nu+ extension for AES

## Slide 37: AES implementation validation
Algorithm for AES128 has been written at assembly level for both version of Nu+
Test vectors generated using OpenSSL library
Core simulation performed using Xilinx XSim

## Slide 38: Result: performance
 | Cycle/byte
Nu+ (ver1) | 4.87
Nu+ (ver2) | 0.83
Intel AES-NI | 1.3
Lane count = 4
Thread count = 4
Synthesis frequency = 200 MHz (Xilinx Zynq-7030 SoC)

## Slide 39: Products
Conference paper:
  A. Cilardo, D. Argenziano “Extending a GPU-like Processor with Montgomery Multiplication Support”, DATE 2018 (pending approval)

## Slide 40
Any questions?