## Slide 1: Giovanni Cavallo Tutor: Dr. Annalisa Liccardo XXX Cycle - I year presentation
THz Imaging based on Compressive Sampling (CS)

## Slide 2: My background
I received the MSc degree in Electronic Engineering (cum laude) from University of Naples, “Federico II”.
I work within “Electrical and Electronic Measurements” DIETI Group (building 3/A, 1st floor, room 1.21)
My fellowship is financed by European Social Fund (ESF)

## Slide 3: Which is the problem?
Traditional methods to acquire and reconstruct signals (or images) are based on the Shannon’s theorem.
The theorem asserts that it is possible to reconstruct, perfectly, a signal, and so without loss information (aliasing), if:
Sample rate fS ≥ 2fMAX
Limitations:
It is impossible to reconstruct a signal if it will be acquired
one-sidedly.
Time of acquisition will be very long if signals have infinite length.

## Slide 4: Solution
Benchmark
To overcome the considered limitations, I have investigated the possibility to move toward a different acquisition method exploiting the advantages of an innovative measurement approach: the Compressive Sampling .
The Compressive Sampling is a new acquisition strategy capable of digitizing the input signal directly in a compressed form, acquiring only a reduced number of samples, but sufficient to successively reconstruct the input signal by means of suitable algorithms
(CVX, L1-Magic , Greedy).

## Slide 5: Compressive Sampling
From a mathematical point of view, spatial–domain sampling of discrete
signals x can be expressed as:
y[M] = A[M x N] * x[N]
y[M]  measurement vector
A[M x N]  sampling matrix
x[N] unknown full resolution image of N pixels
According to CS theory the sampling matrix A can be set as a random matrix of M rows and N columns, whose entries are set uniformly at random equal to 1 or equal to 0.
Reshape

## Slide 6: CS-based THz systems
THz Source
Random Mask
THz Detector
Lens 1
Lens 2
Image to
analyze
The electromagnetic radiation in THz frequency range (0.1–10 THz) can deeply penetrate inside materials. Lower limit: Microwaves. Upper Limit: Far Infrared. No ionizing.
y1
y2
y3
=
x
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0
x1
x2
x3
x4
x5
x6
x7
x8
x9
Unknown Vector x[N]
Sampling Matrix A
y[M]

## Slide 7: CS-based THz systems
The reconstructed vector x’, sparse solution of the problem y=Ax, has to be reordered to finally reconstruct the original image.
Original Image
Reconstructed Vector X
Sparse Solution
0 | 1 | 0
1 | 1 | 0
0 | 1 | 0
Digitized Image
0
1
0
1
1
0
0
1
0
CS Solvers:
CVX
Greedy
TVAL

## Slide 8: Products
Chapter book
“THz measurement system” – Prof. Antonello Andreone, Prof. Leopoldo Angrisani, PhD Student Giovanni Cavallo (in preparation)
Publication
“THz Imaging: advantages and disadvantages of raster scan and compressive sampling” – Prof. Antonello Andreone, Prof. Leopoldo Angrisani, PhD Student Giovanni Cavallo (in preparation)

## Slide 9: Next years…
Research activity
Definition of a model of measurement uncertainly for THz systems;
THz spectroscopy on carbon nanotubes samples in cooperation with DICMAPI of Federico II.
Summary of credits

## Slide 10: Thanks for your attention!!!