## Slide 1: Mirko Gagliardi Tutor: Alessandro Cilardo XXXI Cycle - I year presentation
  Exploring Advanced Computer Architecture and Technique to Improve Performance and Power Efficiency in Many Core Era

## Slide 2
Master of Science:
  In “Ingegneria Informatica” at University of Naples “Federico II”
DIETI Group:
  Seclab
Type of Fellowship:
  Doctoral Fellowship funded by CeRICT
Collaboration:
  With CeRICT in the context of the european project MANGO
Background

## Slide 3: HPC modern trend: GPU-like processors
Problems:
  Power wall, memory wall, ILP wall
  Disruption of the rising of clock frequency
Solutions:
  Heterogeneous platforms, systems made of different computational units, with specialized accelerators that complement general purpose CPUs, such as DSPs, GPUs, co-processors, enabling significant benefits in terms of both power and performance
GPU-like paradigm:
  Match recent trends
  also including FPGA and SoC manufacturers
  Enable higher power-efficiency
  Provide an effective answer to programmability issues
  support for high-level languages and models, like OpenCL
State-of-Art Academic GPU-like core projects
  FlexiGrip, MIAOW GPGPU, Hwacha, Maven

## Slide 4: Nu+ project: configurable GPU-like core
Goal: An open parameterizable architecture for hardware solution exploration
Our Accelerator main focus
  Application-driven accelerator
    Parameterization
  Light Control logic
    More resources for operators
    Power efficient
  64 bit supports register and operators
    In resource sharing
  Custom operation
    Power efficient
  FP and Special Function Unit
  Scratchpad memory support
    Dynamic remapping: reducing bank conflicts
    Power efficient
Relation in MANGO project
  NoC-based manycore architecture Heterogeneous system
  Nu+ will be a compute unit architectures for advanced hardware solution exploration:
    RISC, GPU-like core, special-purpose accelerators
    Microarchitecture-level customization techniques
    Low Power and QoS-aware mechanisms
GN
HN
HN
HN
GN
GN
HN
HN
GN
GN
GN
GN
GN
HN
HN
HN
GN
HN
GN
GN
GN
GN
GN
HN
MANGO: exploring Manycore Architectures for Next-GeneratiOn HPC systems
Nu+
4

## Slide 5: Nu+ Core Overview Main Features
RISC Core
  In-order pipeline semplified control, thread switching to mask latencies
  Parametrization thread number, hardware lane number, ...
  Custom ISA
Multithread support
  Each thread with its own PC
  N hardware lane shared among all threads
    Resourse sharing
High Parallelism
  Scalar and Vectorial
  Each thread has its own registers
  64 bit support (Integer and Floating Point)
    N 32 bit registers or N/2 64 bit registers
Variable latency operator support
  SPM has a variable latency
  Advance Writeback: automatic structural hazard detection

## Slide 6: Results: application-driven customization
Hardware application-driven parameterization
  Each application has an ideal hardware configuration
  E.g. same kernels do not need cache coherence
    In this case a coherent cache is not needed A non coherent scratchpad memory has less hardware overhead
[1] explores hardware ad hoc customization beneficts. We describe how a configurable non coherent memory affects performance and how different parallel kernels require different configurations
Main findings:
  A configurabile non coherent scratchpad memory presented
  Parameterization highly affects performance
  Hardware optimization (Bank Remapping)
    A typically software optimization has been realized in hardware
    Faster than software version
    Minimum overhead and high impact
Next Steps:
  Exploring non-coherent power aware memory solutions
  Custom operators application-driven
  Low Power and QoS-aware mechanisms
6
[1] Cilardo Alessandro, Gagliardi Mirko, Donnarumma Ciro, "A Configurable Shared Scratchpad Memory for GPU-like Processors." International Conference on P2P, Parallel, Grid, Cloud and Internet Computing. Springer International Publishing, 2016.

## Slide 7: Products – Conferences Papers
Cilardo Alessandro, Gagliardi Mirko. "Customizable Heterogeneous Acceleration for Tomorrow's High-Performance Computing." High Performance Computing and Communications (HPCC), 2015 IEEE 7th International Symposium on Cyberspace Safety and Security (CSS), 2015 IEEE 12th International Conference on Embedded Software and Systems (ICESS), 2015 IEEE 17th International Conference on. IEEE, 2015.
Cilardo Alessandro, Gagliardi Mirko, Donnarumma Ciro, "A Configurable Shared Scratchpad Memory for GPU-like Processors." International Conference on P2P, Parallel, Grid, Cloud and Internet Computing. Springer International Publishing, 2016.

## Slide 8: Credits